### Geothermal Heat Pump Heating/Cooling System Details

## I. 	Sizing the System  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 1

## II. 	Costs and Cost Recovery . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 3

## III. 	Actual Usage Numbers  - Heating  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 5

## IV. 	Actual Usage Numbers  - Cooling  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 7

## V. 	Heat Pump Specifications . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 8

## VI.  	DTE D1.2 Rate   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 8

## VII.  	How a Ground Source Heat Pump System Works  . . . . . . . . . . . . . . . . . . . . 9

## VIII.  	Photographs of System Described Here  . . . . . . . . . . . . . . . . . . . . . . . . . . . 10

## I.  Sizing the System

House Description:

Farmhouse built c. 1870, two story with full basement, on 2.3 acres.

Total floor area ~ 2600 square feet

Total window area ~ 3500 square feet

Usual thermostat settings of 66 degrees winter, 79 degrees summer

Fuel Oil usage:

2004/5 heating season consumption was 920 gallons oil

Convert to BTU/yr  -   920 gal/yr * 138048 BTU/gal = 127 million BTU/yr

Oil furnace is c.1970s, 65% efficiency, so actual BTU needed to heat house =

127 million BTU/yr * 0.65 = 81 million BTU/yr =  81 MBTU/yr

Geothermal Unit size required:

Cutoffs are: 	~68 MBTU/yr for 4 tons

~73 MBTU/yr for 5 tons

so 81 MBTU/yr requires 6 tons

Auxiliary Heat elements:

Geothermal unit is sized to provide 90% of heating needs, with an auxiliary electric heating element available for

the remaining 10%.  The 6-ton unit will not quite keep up with heat loss when outside temperature goes below 7

degrees F, but average yearly time below this temperature is only 133 hours, and we felt the added cost (approx

$450 for the 10 KW auxiliary heating element, plus $1000 for upgrade to 150 amp electrical service) was not

justified and portable space heaters can be used if needed.

Water Heater elements:

The desuperheater elements which could be added to provide pre-heated hot water for the electric water heater

were not installed because at 2004-2005 rates of $0.063/kwh our monthly electric water heater bill averages only

$11.  The water heater is now connected to the same meter providing power to the heat pump, so the water heating rate will be $0.096/kwh for 200 kwh/month, or ~ $17/month

Air Conditioning:

The geothermal heat pump also provides air conditioning, which we have not had in the past.  Because the house

remains relatively cool during the day if windows are opened at night, we expect to use air conditioning only an average of 10-20 days per year, for an annual cooling cost of less than $80 + (fixed service charge of 4 mo x $9.50/mo) = $118.

Estimated Electric consumption:

heat pump estimate is 1 kwh/12,000 BTU

To provide 81 million BTU/yr to heat the house (no air conditioning) would require

81 million BTU/yr /12,000 BTU/kwh = 6750 kwh/yr

Using Detroit Edison D1.2 rate of $.096/kwh (ave) + $9.50/month service charge (split evenly

between heat pump and water heater), the annual cost =

6750 kwh/yr * $.096/kwh = $648

+ $9.50/month * 8 months     = $76

---------

$724 (heating for 8 months)

## II.  Costs and Cost Recovery

Costs:  horizontal loop excavation & installation = $1200/ton x 6 tons =   $7200

2-zone damper/control system (2nd floor separately zoned)          $1000

replace supply ductwork in basement                                            $4800

6-ton Water Furnace =                                                                 $10200

install new electrical panel w/70amp circuit                                   $1975

======

$ 25175

Cost Recovery Calculation:

Two Scenarios:  keep the old furnace or replace it with a high-efficiency oil furnace

A.  Keep the Same Oil Furnace

Assumptions made:

Fuel consumption for 2004-2005 heating season is used for the basis.

Oil prices are estimates, based on an annual increase of 12%.

Estimate of oil used each year is the 2004-2005 consumption of 900 gallons.

Oil costs include electricity for the blower (420 kwh/yr * $0.09/kwh = $38/yr).

Cost of electricity is assumed to increase by 2% per year.

Interest lost by spending the money vs. saving it in the bank is not calculated

*Price estimates in italics; actual prices entered as known

The geothermal unit pays for itself after ~8 heating seasons, assuming we keep the same furnace.

B.  Replace the Oil Furnace

Since we needed to replace the ancient furnace and ductwork anyway, at an estimated cost of:

$4000 (90% efficiency furnace)

$4800 (ductwork)

$1000 zoning control

--------

$9800

the differential cost of going to geothermal is:

$25175 (total project)– 9800  = $15375

Assumptions made:

Fuel consumption for 2004-2005 heating season is used for the basis.

Oil prices are estimates, based on an annual increase of 12%.

Annual oil consumption estimate recalculated using a furnace efficiency of 90% instead of 65%:

Interest lost by spending the money vs. saving it in the bank is not calculated

81 million BTU/yr needed / 0.9 efficiency = 90 million BTU/yr burned

90 million BTU/yr * 1 gal oil/138,000 BTU = 652 gal/yr

A more efficient blower is assumed, using only 300 kwh/hr instead of 420 kwh/yr

electricity cost for the blower = 300 kwh/yr * $0.09/kwh = $27/yr

Cost of electricity is assumed to increase by 2% per year.

*Price estimates in italics; actual prices entered as known

The geothermal unit pays for itself in just over 7 heating seasons when using the differential cost vs upgrade

to a new high efficiency oil furnace.

## III.  Actual Usage Numbers  - Heating  :

Estimating oil usage through degree days:

For oil in 2004-5, 918 gal/yr / 6550 DD/yr = 0.14 gal/DD

At a 2005 oil price of $2.75/gal, this is $0.39 per degree day

Heat pump is about  (6750 kwh)/(5746 DD) = 1.17 KWH / degree day.

At an average of $0.096/kwh this is $.11 per degree day.

For the 2005-06 heating season, at $3/gal, oil would have cost

$.39/DD * 5748 DD = $2241 , which is about 2.6 times the $869 spent on the heat pump for the heating season

By 2012 the estimate is oil will be nearly 6 times as expensive.

## IV.  Actual Usage Numbers  - Cooling :

There is no comparable cost data for cooling in the past because there was no central air conditioning in past years.

Electricity cost for the fans and window air conditioning used occasionally would have been insignificant.

## V.  Heat Pump Specifications:

Water Furnace Premier E Series E072T

Dual-capacity compressor		R-410A refrigerant (non-ozone-depleting)

EER to 25 and COP to 4.7		Honeywell duct-mounted humidifier

88,000 BTU cooling

65,000 BTU heating

Electrostatic cleanable air filter 90% eff. down to 1 micron

10 yr warranty all parts

Horizontal Closed Loop System

80% conditioned water, 20% methyl alcohol

10 yr warranty for leaks

piping buried in trenches~300 feet long, 5’ deep

Piping is high density polyethylene, fused joints

Contractor:  Michigan Energy Services		888-339-7700

Rob Derksen

8445 Main St.

Whitmore Lake, MI 48189

## VI.  DTE D1.2 Rate:

Peak hours - 10 a.m. - 7 p.m.

Summer cooling (June-Sept) - peak        $0.126/kwh electric + $0.044 delivery + $0.02 surcharges = $0.188/kwh

off-peak   $0.03/kwh electric + $0.044 delivery + $0.02 surcharges =  $0.094/kwh

Heating (Oct-May)    -  peak       $0.07/kwh electric + $0.044 delivery + $0.02 surcharges =  $0.1334/kwh

off-peak  $0.02/kwh electric + $0.044 delivery + $0.02 surcharges =   $0.084/kwh

Our usage: 75% off-peak, 25% peak    Ave. daily rate = .75(.084)+.25(.1334) = $0.096/kwh (heating)

= .75(.094)+.25(.188) =  $0.117/kwh (cooling)

Monthly service charge is $19.00 (prorated evenly between water heater and heat pump)

## VII.  How a Ground Source Heat Pump Works

(This account comes from a residential application in Ontario but the numbers are very similar to ours)

Geothermal heating and cooling is based on one simple fact: that 6 feet down in the ground the temperature is the same—between 50˚F and 60˚F- the whole year round. This means that it is relatively cool in the summer, and relatively warm in the winter. Geothermal heating is thus quite different from solar heating: solar heating works worst when you most need it--in the cold, cloudy, snowy conditions of winter; the source for geothermal heating and cooling is not affected by the weather.

For geothermal cooling, all one needs to do is to circulate water in a pipe through the ground to cool it, and use this cool water to cool the air pumped through the house in the heating ducts.

For heating, there is an extra wrinkle. Most of us prefer the temperature in the house in the winter to be nearer 70˚F than 60˚F, so we need to raise the temperature of the relatively warm air a little. For this we use the gas equation that you may remember from High School Physics: PV=RT. Here P is pressure, V is volume, T is absolute temperature, and R is a constant. If we keep the volume constant, we see that the Pressure is proportional to the Temperature. This means that if we want to raise the temperature of the air a little, then we should increase its pressure a little. To see how much, we must work in absolute temperature, which is 273˚+temperature in Celsius (centigrade) . Take an example: suppose the temperature of the water coming out of the ground were 50˚F; that is 10˚C or 273˚+10˚=283˚ absolute. We want to heat the air from 50˚F to say 68˚F. 68˚F is 20˚C or 273˚+20˚=293˚ absolute. Raising the temperature from 283˚ to 293˚, means that we raise it by (293-283)*100/283 percent, or 3.5 %. That small increase in pressure can easily be done by using a compressor.

That is the theory. Now the technology. First we have to build a trench in which to place the pipes carrying the water (actually they add some glycol to it, to improve the performance). For our installation we had 3 trenches each 300ft long, 5ft wide and 5ft deep. Each trench had four 4inch pvc pipes in it; 3600 ft in all. Typically the trenches are 5ft deep, rather than 6ft, because all kinds of safety regulations come into play in building a 6ft trench. The 4inch pipes are fed from one large pipe coming from the basement, and they are funnelled back into a large pipe as they return to the basement. The whole system is filled with water and sealed. There is a pump in the basement that circulates the water through the pipes, and brings the warm water back into the basement. The water then goes into a heat exchanger. A heat exchanger does just that: it takes the heat out of the water and heats air that runs through pipes through the water. A heat exchanger is rather like two clasped hands, with the fingers of one hand interleaved with the fingers of the other. One set of fingers carries the warm water, the other carries the air to be heated.

After being heated by the water, the air enters a compressor where it is warmed further, before feeding it into the air ducts. It is possible to have the pipes running deep down into the ground, rather than running horizontally 5ft down. If there is a lake or a deep river, then the pipes can run through the water, rather than through the ground.

Now the money matters. We live in the country. In the winter of 2004/5 we spent about $2,500 on oil for our oil furnace. If we had kept the furnace, then we would have spent about $3,000 in the winter of 2005/6. The geothermal system has four parts: the pump to move the water around the circuit, the compressor, the heat exchanger, and the fan to blow the air through the house; those cost $18,000. The trench and pipes cost $2,000, and the necessary changes to the electrical system in the house cost another $2,000. We received a rebate of $600 on the items from the Ontario Government, and another $1,400 from a government conservation initiative.

When the system is running at moderate strength it takes 1500 KWH, about the same as a single baseboard heater; when it is running at high, it uses 2200KWH, and when the fan alone is working, then it uses 500KWH. Our electrical bill has increased by about $150 per month for the winter months.

We did not have air conditioning before; the air conditioning is set to come on when the temperature in the house reaches 75˚F, which is not often. The biggest difference in the winter months is in the quality of the air inside the house. There is now no combustion, so no loss of oxygen, as there is with an oil furnace. As far as conservation is concerned, we save about 8 tons of carbon dioxide per year!

A few additional points. Obviously geothermal doesn’t work for everyone. My father has a luxury of a large backyard, so he could fit all that piping easily into shallow trenches. If you don’t have that much room, as he points out, you have to dig down—and that’s obviously more expensive. I’m not suggesting, in other words, that this is going to solve the energy crisis. But surely there are lots of lots of houses—as well as commercial buildings (like malls, with huge parking lots) that could easily install geothermal systems, and even a modest application of technologies like this could begin to make a real difference in our energy problems.

I think it is also worth noting how absurdly low-tech the system is. It is pvc pipes and a compressor. My father lives in Ontario, where the winters can be vicious, and has thrown out his furnace! The other noteworthy fact is how (relatively) inexpensive the system is. For an investment of $25,000, my father saves, conservatively, $2000 a year (remember; he wasn’t running air conditioning in the summer before this, so the financial benefits of his system are substantially understated.

Polyethylene pipe sample

Trenching along west edge of yard

Several loops in yard converge at this hub area and go into house

Ground loops as they enter the house about 3’ below the surface

Ground loops as they enter the basement, with 1” foam insulation

Heat pump unit, about the size of a refrigerator; ground loops enter at bottom right.

# Text boxes

| Same Furnace Oil heat Heat pump Savings Cume Year Oil per gal* $ per yr $ per yr $ per yr Savings $ 2005-6 $2.75 2513 724 1789 1789 2006-7 $2.99 2729 738 1991 3780 2007-8 $3.35 3052 753 2299 6078 2008-9 $4.75 4313 768 3545 9623 2009-10 $5.32 4826 784 4042 13665 2010-11 $5.96 5401 799 4601 18266 2011-12 $6.67 6044 815 5229 23495 2012-13 $7.47 6765 832 5933 29428 |  |  |  |  |
| --- | --- | --- | --- | --- |

| Replace Furnace Oil heat Heat pump Savings Cume Year Oil per gal* $ per yr $ per yr $ per yr Savings $ 2005-6 $2.75 1820 724 1096 1096 2006-7 $2.99 1976 738 1238 2334 2007-8 $3.35 2210 753 1457 3791 2008-9 $4.75 3124 768 2356 6147 2009-10 $5.32 3496 784 2712 8859 2010-11 $5.96 3912 799 3113 11971 2011-12 $6.67 4378 815 3563 15534 2012-13 $7.47 4900 832 4069 19603 |  |  |  |  |
| --- | --- | --- | --- | --- |

| On Peak Off peak Monthly Cume Degree $/DD kwh kwh $ $ Days 2007-08 Heating Season Oct 07 7 142 $21 $21 357 $0.06 Nov 07 221 635 $91 $113 819 $0.11 Dec 07 420 1237 $168 $281 1167 $0.14 Jan 08 535 1531 $208 $489 1201 $0.17 Feb 08 400 1599 $196 $685 1258 $0.16 Mar 08 377 1379 $174 $860 1011 $0.17 Apr 08 39 426 $49 $909 444 $0.11 May 08 8 146 $22 $931 329 $0.07 -------- -------- Total= 9102 kwh 6586 $0.13 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| On Peak Off peak Monthly Cume Degree $/DD kwh kwh $ $ Days 2005-06 Heating Season Oct 05 13 26 $12 $12 406 $0.03 Nov 05 234 702 $99 $111 694 $0.14 Dec 05 500 1500 $201 $312 1223 $0.16 Jan 06 280 1204 $147 $459 982 $0.15 Feb 06 620 1613 $227 $685 1102 $0.21 Mar 06 433 1012 $151 $837 905 $0.17 Apr 06 72 169 $32 $869 436 $0.07 -------- -------- Total= 8137 kwh 5748 $0.15 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| On Peak Off peak Monthly Cume Degree $/DD kwh kwh $ $ Days 2006 Cooling Season May 06 14 33 $13 $13 59 $0.22 Jun 06 3 6 $9 $23 93 $0.10 Jul 06 130 190 $42 $64 275 $0.15 Aug 06 80 116 $29 $93 159 $0.18 Sep 06 46 137 $26 $119 14 $1.87 ------ ------ Total: 755 kwh 586 $0.20 Sep 06 46 137 $26 $119 14 $8.53 ------ |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

| On Peak Off peak Monthly Cume Degree $/DD kwh kwh $ $ Days 2007 Cooling Season May 07 18 43 $15 $15 244 $0.06 Jun 07 67 119 $27 $42 184 $0.15 Jul 07 65 68 $23 $65 136 $0.17 Aug 07 214 133 $48 $113 247 $0.20 Sep 07 59 50 $20 $134 210 $0.10 -------- -------- Total: 835 kwh 811 $0.16 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

| On Peak Off peak Monthly Cume Degree $/DD kwh kwh $ $ Days 2006-07 Heating Season Oct 06 53 502 $58 $58 576 $0.10 Nov 06 187 695 $92 $149 712 $0.13 Dec 06 405 1082 $153 $303 931 $0.16 Jan 07 505 1366 $190 $493 1193 $0.16 Feb 07 407 1699 $205 $699 1332 $0.15 Mar 07 222 990 $121 $820 788 $0.15 Apr 07 142 603 $78 $898 606 $0.13 -------- -------- Total= 8858 kwh 6138 $0.15 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| On Peak Off peak Monthly Cume Degree $/DD kwh kwh $ $ Days 2008 Cooling Season May 08 0 0 $0 $0 11 $0.00 Jun 08 33 38 $16 $16 130 $0.12 Jul 08 148 73 $34 $50 200 $0.17 Aug 08 130 130 $37 $87 147 $0.25 Sep 08 2 80 $15 $102 135 $0.11 -------- -------- Total: 634 kwh 623 $0.16 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |

|  | On Peak | Off peak | Monthly |  | Cume | Degree | $/DD |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | kwh | kwh | $ |  | $ | Days |  |

| 2008-09 Heating Season |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Oct 08 | 66 | 331 | $45 |  | $45 | 509 | $0.09 |
| Nov 08 | 233 | 899 | $115 |  | $160 | 822 | $0.14 |
| Dec 08 | 339 | 1527 | $182 |  | $342 | 1217 | $0.15 |
| Jan 09 | 610 | 1939 | $253 |  | $594 | 1525 | $0.17 |
| Feb 09 | 387 | 1459 | $183 |  | $777 | 1064 | $0.17 |
| Mar 09 | 266 | 1211 | $146 |  | $923 | 868 | $0.17 |
| Apr 09 |  |  |  |  |  |  |  |
| May 09 |  |  |  |  |  |  |  |
|  |  |  |  |  |  | -------- | -------- |
|  | Total= | 9267 kwh |  |  |  | 6005 | $0.15 |