# Residential Heat Loss and Heat Gain Calculation

## I.  Present setup, assume Poor infiltration

## Design Conditions:  Williamston

Indoor:					Outdoor:

Summer Temperature:   	78		Summer Temperature:	87

Winter Temperature:		65		Winter Temperature:		1

Relative Humidity:		50		Summer Grains Moisture:	95

Daily Temp Range:	      Medium

Building Component		Sensible	Latent		Total		Total

Gain		Gain	       	Heat Gain     	Heat Loss

(BTUH)	(BTUH)	(BTUH)	(BTUH)

-------------------------------------------------------------------------------------------------------

Whole House			22,457		3,665		26,122		81,426

(2 tons)

-------------------------------------------------------------------------------------------------------

First Floor			13,642		2,597		16,239		48,452

Living Room		  5,698		   763		  6,461		17,772

Front Entry		  2,334	 	   508		  2,842		  7,562

Laundry		  1,277		   379		  1,656		  6,504

Bathroom 		     545		     61		     606		  1,711

Dining Room		     535		   197		     732		  3,701

Kitchen		     946		   136	 	  1,082		  2,715

Alcove			  1,277		   303		  1,580		  4,342

Study			  1,030		   250		  1,280		  4,145

Second Floor			  7,437		   772		  8,209		15,853

Bathroom		  1,208		   189		  1,397		  3,082

Guest bedroom	     773		   174		     947		  3,185

Master bedroom	  1,569		   174		  1,743		  3,575

Sunroom		  3,089		   167		  3,256		  4,213

Stairwell		     798		     68	  	     866		  1,798

Basement

Water heater room	     479	 	     61		     540		  6,315

Furnace room		     166		       0	 	     166		  3,075

Root cellar		     732		   235		     967		  7,728

-------------------------------------------------------------------------------------------------------

## Whole House			22,457		3,665		26,122		81,426

## II.  For case:  Average infiltration

## Whole House			22,150		3,180		25,330		74,853

savings of 6573 BTUH = 8.0 %

III.  Replace Living Room, Study w/high efficiency windows + Average Infiltration

## Whole House			22,070		3,180		25,257		74,642

savings of 211 BTUH = 0.3 %

Calculations done with HVAC-Calc Residential 4.0